## Slide 1: Wastewater Alert methodology
​County Alert Criteria:
Date | Days since last report | Wastewater | Past 8 period rolling average
2022-01-07 | NA (first report) | 100 | NA
2022-01-14 | 7 | 120 | NA
2022-02-04 | 28 | 120 | NA
2022-02-11 | 7 | 120 | NA
2022-02-18 | 7 | 80 | NA
2022-03-04 | 14 | 100 | NA
2022-03-11 | 7 | 80 | NA
2022-03-18 | 7 | 100 | NA
2022-04-01 | 14 | 100 | 102.5
2022-04-08 | 7 | 100 | 102.5
2022-04-15 | 7 | 120 | 100
2022-04-22 | 7 | 140 | 100
Date | Days since last report | Wastewater | Past 8 period rolling average
2022-01-07 | NA (first report) | 100 | NA
2022-01-14 | 7 | 120 | NA
2022-02-04 | 28 | 120 | NA
2022-02-11 | 7 | 120 | NA
2022-02-18 | 7 | 80 | NA
2022-03-04 | 14 | 100 | NA
2022-03-11 | 7 | 80 | NA
2022-03-18 | 7 | 100 | NA
2022-04-01 | 14 | 100 | 102.5
2022-04-08 | 7 | 100 | 102.5
2022-04-15 | 7 | 120 | 100
2022-04-22 | 7 | 140 | 100
Each alert is based on the rolling 8-period mean and standard deviation
Notes: Each alert is going to be based on the rolling 8-period mean and standard deviation of the wastewater values for that county, as shown in the table.

## Slide 2: Wastewater Alert methodology
​County Alert Criteria:
Date | Days since last report | Wastewater | Past 8 period rolling average
2022-01-07 | NA (first report) | 100 | NA
2022-01-14 | 7 | 120 | NA
2022-02-04 | 28 | 120 | NA
2022-02-11 | 7 | 120 | NA
2022-02-18 | 7 | 80 | NA
2022-03-04 | 14 | 100 | NA
2022-03-11 | 7 | 80 | NA
2022-03-18 | 7 | 100 | NA
2022-04-01 | 14 | 100 | 102.5
2022-04-08 | 7 | 100 | 102.5
2022-04-15 | 7 | 120 | 100
2022-04-22 | 7 | 140 | 100
Date | Days since last report | Wastewater | Past 8 period rolling average
2022-01-07 | NA (first report) | 100 | NA
2022-01-14 | 7 | 120 | NA
2022-02-04 | 28 | 120 | NA
2022-02-11 | 7 | 120 | NA
2022-02-18 | 7 | 80 | NA
2022-03-04 | 14 | 100 | NA
2022-03-11 | 7 | 80 | NA
2022-03-18 | 7 | 100 | NA
2022-04-01 | 14 | 100 | 102.5
2022-04-08 | 7 | 100 | 102.5
2022-04-15 | 7 | 120 | 100
2022-04-22 | 7 | 140 | 100
Values are not considered if they include a reporting gap of over 14 days
Notes: Alerts will not be generated if the rolling 8-period values include any reporting gap of over 14 days, so here we see that since there was a gap in reporting of 28 days form January 14 to February 4, we won’t be able to generate any alerts until April 15, when we have a full 8 prior periods without a gap of more than 14 days.

## Slide 3: Wastewater Alert methodology
​County Alert Criteria:
Date | Days since last report | Wastewater | Past 8 period rolling average
2022-01-07 | NA (first report) | 100 | NA
2022-01-14 | 7 | 120 | NA
2022-02-04 | 28 | 120 | NA
2022-02-11 | 7 | 120 | NA
2022-02-18 | 7 | 80 | NA
2022-03-04 | 14 | 100 | NA
2022-03-11 | 7 | 80 | NA
2022-03-18 | 7 | 100 | NA
2022-04-01 | 14 | 100 | 102.5
2022-04-08 | 7 | 100 | 102.5
2022-04-15 | 7 | 120 | 100
2022-04-22 | 7 | 140 | 100
Wastewater | Past 8 period rolling average | Past 8 period rolling std dev | Threshold
330.697 | 317.426 | 29.7466 | 724.092
347.765 | 318.376 | 30.0731 | 726.971
297.476 | 317.289 | 28.6221 | 720.444
317.434 | 314.695 | 29.4531 | 717.75
331.388 | 311.216 | 26.8548 | 702.996
395.916 | 312.534 | 27.642 | 707.994
534.04 | 328.27 | 34.8743 | 432.893
640.068 | 354.155 | 80.6161 | 596.003
873.77 | 399.348 | 122.579 | 767.086
1441.58 | 467.232 | 203.075 | 1076.46
1510.37 | 603.958 | 391.735 | 1779.16
2184.6 | 755.571 | 480.768 | 2197.87
Once mean and standard deviation are calculated, a threshold value is created, and an alert will be generated when the wastewater value is above the threshold
Notes: When we have the required wastewater data to generate the alerts, the mean and standard deviation are calculated and a threshold value is created from them. An alert is generated when the wastewater value is above the threshold set. In the case of this example, that would mean each of the highlighted rows would be showing an alert.

## Slide 4: Wastewater Alert methodology
​Threshold value equation:
If Wastewater value for the current row is > 500:
Threshold = Rolling Mean + 3 * Rolling Standard Deviation
If Wastewater value for the current row is < = 500:
Threshold = 2 * Rolling Mean + 3 * Rolling Standard Deviation
Notes: The threshold equations are split by how large the wastewater value is. If the wastewater data for the current day is above 500, then the calculation is the rolling mean plus 3 standard deviations, which is a standard anomaly detection equation. However, if the wastewater data for the current day is less than or equal to 500, then the calculation is 2 rolling means plus 3 standard deviations. This split was created because too many alerts were being generated when wastewater was low due to normal volatility.

## Slide 5: Wastewater Alert methodology
​Alert priority classification:
Low:
If current bed count is less than 5
Medium:
If current bed count is greater than or equal to 5
High:
If medium criteria is met plus there was an alert in the last period as well
Notes: The last component of the alerts is the prioritization of them. We noticed when bed values were very low, the spike that wastewater was predicting was usually negligible. An example is an alert that was generated for Suffolk County, MA that preceded a spike in beds from an average of less than 1 to an average over 6. While the alert is still valid, the urgency behind it is not. Thus, we decided to implement a ranking system in the alerts so any time the current count of beds was below 5 it would automatically be listed as Low priority, whereas current bed values of greater than 5 would bump the priority up to Medium. A High priority alert only occurs when beds are above 5 and there was also an alert in the prior reporting period, since a sustained spike in wastewater is more likely to be indicative of a large spike in beds to come.